## Slide 1
DDoS 攻擊進階防護
A10 台灣區技術經理 陳志緯
Notes: Attack duration is more than 24 hours on average, sometimes lasting weeks. During this time a lot of collateral damage happens to the business; overloaded customer support, delayed projects etc.
http://www.forbes.com/2010/02/01/brand-reputation-value-leadership-managing-ethisphere.html
£100,000/hr Neustar, 2015
$40,000/hour Incapsula, 2014
$22,000/minute average Ponemon, 2015
Reputation damage
Avg. attack duration: >24hrs Akamai
http://security.radware.com/uploadedFiles/Resources_and_Content/Attack_Tools/CyberSecurityontheOffense.pdf
https://www.stateoftheinternet.com/downloads/pdfs/2015-ponemon-institute-the-cost-of-ddos-attacks.pdf
Ponemon: check 2015
£100,000/hr Neustar, 2015
$40,000/hour Incapsula, 2014
$22,000/minute average

## Slide 2: DDoS 攻擊持續演進
單一型攻擊
網路層攻擊
  Fragmentation
  SYN floods
  Ping floods
  …
應用層攻擊
  Slowloris
  HTTP GET floods
  R.U.D.Y.
  …
放大攻擊
  DNS amplification
  NTP amplification
  …
複合型攻擊
複合型攻擊
  網路層攻擊
  應用層攻擊
  …

## Slide 3: 電信商遭受 DDoS 攻擊事件
DDoS 攻擊流量
  300Mbps / 200K CPS / 2M Concurrent Sessions
多層次 DDoS 攻擊 (複合型 DDoS Attacks)
  Network Attack (網路層攻擊)(ICMP)
  Amplification Attack (放大攻擊)(DNS-UDP)
  Resource Attack (資源耗損攻擊) (TCP)
  Application Attack (應用層攻擊) (HTTP Slowloris)
應用層攻擊 特性說明 :
  Attacker 透過殭屍網路(Botnet)(90% from TW)發起大量TCP連線及HTTP Request封包 (~1K conns per bot )
  對於防火牆而言屬於正常連線存取
  防火牆效能下降及 Server 資源耗盡。
Customer Data
Web Apps
DDoS
DDoS
DDoS
DDoS
DDoS
DMZ
Secure from Outside
Internal LAN
!
ADC
Notes: All data based on list prices

## Slide 4: DNS 放大攻擊 (Amplification)
Attacker
Request With spoofed Src IP
Open DNS Resolver
Request Packet Size = 32 bytes
Response Packet Size = 3200 bytes
Response
DDoS
DDoS
DDoS
DDoS
DDoS
Source: IDG, 2016

## Slide 5: DNS NXDomain 攻擊
Source: IDG, 2016
NXDomain Requests with spoofed Src IP
NXDomain Recursive
DNS Cache
root(.) / TLD / Auth DNS
Attacker
Remote Control
DDoS
DDoS
DDoS
DDoS
DDoS
Zombies

## Slide 6: HTTP GET Flood / TCP Flood 攻擊
Source: IDG, 2016
Attacker
Remote Control
1000 conns per zombie
2M conns
(2K zombies)
DDoS
DDoS
DDoS
DDoS
DDoS
Zombies

## Slide 7: HTTP Slowloris 攻擊
Source: IDG, 2016
Attacker
Remote Control
Uncompleted HTTP Requests
DDoS
DDoS
DDoS
DDoS
DDoS
Zombies

## Slide 8: SSL Renegotiation / SSL Conn Flood 攻擊
Source: IDG, 2016
Attacker
Remote Control
SSL Renegotiation &
SSL Authentication
DDoS
DDoS
DDoS
DDoS
DDoS
Zombies

## Slide 9: DDoS 攻擊來源
Source: Kaspersky , Q3 2015
DDoS
DDoS
DDoS
DDoS
DDoS
Notes: All data based on list prices

## Slide 10: DDoS 攻擊來源 – CCTV 影像監視系統
Source: SUCURI BLOG , Q2 2016
Notes: All data based on list prices

## Slide 11: DDoS 攻擊目標
Source: Akamai Q4 2014
Notes: All data based on list prices

## Slide 12: 頻寬型 DDoS 攻擊
Source: Akamai
1 Gbps DDoS Traffic :
SYN Flood (0.5Kb) : 2M PPS
ICMP Flood(2Kb) : 500K PPS
DNS Flood (10Kb) : 100K QPS
UDP Flood (2Kb) : 500K PPS
Notes: All data based on list prices

## Slide 13: DDoS 攻擊類型比例
Source: IDG, 2016
DDoS
DDoS
DDoS
DDoS
DDoS
Notes: All data based on list prices

## Slide 14: 多層次(Multi-Layer) DDoS 防禦網路
14
Core Network
Data Center
Services
Traffic Redirection
Thunder TPS CPE
Thunder TPS CPE
Services
Scripts / Manual Action
Signaling
Verisign
OpenHybrid
Scripts / Manual Action
Signaling
Huge Bandwidth Attack
High Latency ?
Poor Customization ?
Bandwidth Attack
Low Latency
Limited Customization ?
Huge Bandwidth Attack ?
No Latency
Full Customization
Bandwidth Attack ?

## Slide 15: 多層次(Multi-Layer) DDoS 防禦網路
15
Core Network
Data Center
Services
aXAPI / Manual Action
Traffic Redirection
Telemetry
Thunder TPS CPE
Thunder TPS CPE
Services
Cloud
OpenHybrid
頻寬型攻擊
頻寬型攻擊
網路層攻擊
網路層攻擊
應用層攻擊
Detector

## Slide 16: 用戶端防禦架構 (CPE)
Flood Thresholds
Protocol Anomalies
Behavioral Anomalies
Resource Starvation
L7 Scripts
Black Lists
Real-time Detection
HTTP
DNS
TCP
UDP
Services
Detector
Telemetry
網路層攻擊
應用層攻擊
Notes: Inline provides much more traffic statistics since we see the return traffic. Also, the need for 3rd party flow analysis is reduced or eliminated. They can provide extra value for real-time threshold tuning, reporting etc.
Can be used to scale firewall or existing DDoS mitigation device

## Slide 17: ISP 端流量清洗中心(Clean Pipe)
Web Server
Genie ATM
BGP Router
User
Attacker
Router
BGP Route Injection
Flow
sFlow
Flow
Bot
Thunder TPS
頻寬型攻擊
網路層攻擊
Notes: This is the classic deployment model. Popular when customers only want an extra element in path of traffic only when really necessary. But mostly done to oversubscribe mitigation vs uplink bandwidth, classic mitigation solutions can’t scale andare very expensive. Due to its capacity and performance, Thunder TPS is uniquely positioned to be in the path of traffic all the time for always-on protection
Partners for flow-based detection: FlowTraq and GenieNRM

## Slide 18: 雲端流量清洗中心(Cloud Clean Pipe)
TPS
Verisign
OpenHybrid
API Call
Data Center
頻寬型攻擊

## Slide 19: DDoS 攻擊偵測與防禦
透過五道防護，有效阻絕複合型 DDoS 攻擊
異常封包檢測 :
Network level packet sanity check (conformance)
連線驗證:
Network and application level validation of client origination integrity
黑白名單:
Network level high speed inspection and control
流量管控:
  Network and application monitoring to rate limit traffic
應用層檢測:
Network and application

## Slide 20: 異常封包檢測
Packet sanity check in hardware and software
  Prevents volumetric attacks and protocol attacks
  Network checks (L3-4) for standard behavior
Examples
  TCP SYN & FIN,
  TCP XMAS (URG + FIN + PSH flags),
  LAND Attack (source IP = destination IP),
  TCP Bad Checksum,
  UDP Bad Checksum,
  more…
Denied
Allowed
Packet Anomaly
Inspection
hping3 10.10.10.10 –s 80 –p 80 –S –a 10.10.10.10 –-flood

## Slide 21: 黑白名單
High speed inspection and control of good and bad sources
  Prevents known bad clients
  8 x 16 M entries list capacity
  Network level enforcement (L3-4)
Examples
  Import 3rd Black/White Lists,
  Dynamic White List creates from SYN Cookie, SYN authentication & Action-on-ACK, DNS authentication
  Dynamic Black List with scanning detection, TCP abnormal packets threshold, HTTP header filter, more…
Denied
Allowed
Large List Look-up
With Multiple Actions
Known Bad IP

## Slide 22
保護網路以避免未來的威脅
封鎖非 DDoS 相關威脅，例如垃圾郵件與網路釣魚
提高 Thunder TPS 效率
透過 ThreatSTOP 提供
A10 威脅情報服務
Dynamic Threat Intelligence Cloud
Detect
Correlate
Validate
Dynamic Threat Intelligence Updates
Reputation Lists
Bad Actors
Honeypots
Malware Lists
Dshield Abuse.ch Shadowserver
More...
22
Thunder TPS
Thunder TPS
Thunder TPS
Thunder TPS
Powered by ThreatSTOP
Notes: A10 Threat Intelligence Service is an optional service subscription for Thunder TPS. It takes information for many feeds that get correlated, and mixed with their own intelligence based on honeypots and customer logs

## Slide 23: 連線驗證
Validates client origination integrity
  Bot detection
  Prevents volumetric and protocol attacks
  Network and application checks (L3-7)
Examples
  TCP SYN authentication,
  TCP SYN cookie,
  UDP authentication,
  DNS authentication,
  HTTP Challenge,
  TCP error packet limit, more…
Denied
Allowed

## Slide 24: TCP SYN Cookie
TCP SYN
S=X
TCP SYN
TCP SYN-ACK
S=Z, A=X+1
TCP ACK
S=X
S=X+1, A=Z+1
Data Traffic
If Seq & Ack are valid,
then White List
TCP SYN-ACK (SYN Cookie)
S=Y, A=X+1
Key(server) + client addr + client port + server addr + server port → hash = Y
Valid TCP ACK
S=X+1, A=Y+1
If Key(server) + client addr + client port + server addr + server port → hash = Y , then valid

## Slide 25: TCP Authentication
TCP SYN
TCP SYN
TCP SYN-ACK
TCP ACK
If Seq & Ack are valid,
then White List & Send RST
TCP SYN-ACK
Valid TCP ACK
TCP RST

## Slide 26: HTTP Authentication
HTTP Request
HTTP 302 code w/ cookie
HTTP Request w/ cookie
Check HTTP Request
Valid : Forward
Invalid : Drop
TCP 3-way Handshake
TCP 3-way Handshake
HTTP Request

## Slide 27: 流量管控
Monitor and rate limit traffic
  Network and application level enforcement (L3-7)
  Configurable over-limit actions for TCP, UDP, HTTP and DNS
  Rate limit per connection (TCP or UDP) for ultra-granular control
  Bandwidth or packet rate control
Examples
  Connection limit,
  Connection rate limit,
  Fragment rate limit,
  Packet rate limit,
  Bandwidth limit,
  HTTP Request rate limit,
  DNS request limit per DNS Record Type,
  SSL request rate limit, more…
Rate and/or Connection
Limits for Predictable Load

## Slide 28: 偵測頻率( 0.1sec vs 1sec)
Rate interval = 1 sec
Rate limit = 10K / 1 sec = 1K / 0.1sec
Attack (Burst) : 10K / 0.1sec
Passed :10K , Dropped : 0K
10K
0.1sec
Passed
dropped
5K
1sec
Rate interval = 0.1 sec
Rate limit = 1K / 0.1sec = 10K / 1sec
Attack (Burst) : 10K / 0.1sec
Passed :1K , Dropped : 9K
10K
0.1sec
Passed
dropped
5K
1sec
1K

## Slide 29: 應用層行為檢測
Monitor and check traffic behavior
  400+ global, destination-specific and behavioral counters
  All counters available through GUI, CLI, sFlow export
  Enforce specific values
  Network and application checks (L3-7)
Examples
  TCP template, HTTP template, DNS template, UDP template, SSL-L4 template, Scan detection, aFleX scripting, more…
  HTTP Slowloris
  SSL authentication as bot detection
  SSL Renegotiation
Denied
Allowed
DPI and Application
Awareness for
L7 Protection

## Slide 30: SSL Handshaking
1. Request server public certificate
2. Server public certificate
Server public certificate (key)
Private Key (Signed by CA)
Server certificate Validation
symmetric key
symmetric key
3. Send symmetric key
Symmetric Encryption (256 bits)
(Data)
SHA-256(SHA-2)
Asymmetric Encryption (2048 bits)

## Slide 31: SSL Renegotiation
Client Hello
Server Hello
Send Symmetric Key
Send Symmetric Key
Send Symmetric Key
Send Symmetric Key
Send Symmetric Key
TCP RST
TCP RST
Server public certificate (key)
Private Key (Signed by CA)

## Slide 32: SSL Authentication
Client Hello
If pass SSL Authentication,
then White List & send RST
Server Hello
Send Symmetric Key
Server public certificate (key)
Private Key (Signed by CA)
Client Hello
Server Hello
Send Symmetric Key
Encrypted Data
TCP RST

## Slide 33: DNS Security
  DNS authentication
  Drop ANY query
    any-check
  DNS Query Check
    malformed-query-check (basic or extended)
  FQDN max label length per suffix
    fqdn-label-length
  FQDN request rate limit
    fqdn-rate-limit (per suffix)
  NXDOMAIN request rate limit
    nxdomain-rate-limit
  Filter
    UDP/TCP payload filter (e.g. regex) can be used
  Per record type request rate Limit
    A
    AAA
    CNAME
    MX
    NS
    SRV
    Type value <1-65535> e.g. 255=ANY
  Over limit action
    Activate DNS authentication once request rate exceeded the limit
    Triggered by
    Per record type request rate limit
  And more…

## Slide 34: DNS NXDomain Mitigation
NXDomain Requests
NXDomain Response
DNS Cache
NXDomain Requests
NXDomain Response
NXDomain Requests
NXDomain Response
If NXDomain >= 3 per second ,
then Black List or Rate Limit
NXDomain Requests
X

## Slide 35: HTTP Security
  HTTP challenge
  HTTP protocol malformed check
    Bad chunk, Max length for content, header name, header line and request line, and max number of headers
  Slow and low attack mitigation
    idle-timeout
    mss-timeout : R.U.D.Y / SlowPOST (long form submission)
    request-header timeout : Slowloris
    slow-read-drop : SlowREAD
  Filter
    Filter-header : Regex filter, Byte offset filter for HTTP header (up to 5 filters in one template)
    Filter based on http-referer, user-agent
    Black list action available
  Request rate limit
    Total HTTP request rate limit
    Per URI request rate limit
    Response rate limit (w/ response size)
  Over limit action
    Activate HTTP challenge once request rate exceeded the limit
    Triggered by
      Total HTTP request rate limit
      Response rate limit
  And more…

## Slide 36: HTTP Slowloris
HTTP Request ( 1/2 )
TCP 3-way Handshake
HTTP Request ( 2/2 )
TCP 3-way Handshake
HTTP Request ( 1/2 )
HTTP Request ( 2/2 )
HTTP Request ( 1/2 )
Request header timeout, Then drop or black list
X

## Slide 37: Slow READ ( TCP Zero Window)
HTTP Request ( window = 0 )
TCP 3-way Handshake
TCP ACK ( window = 0 )
TCP 3-way Handshake
HTTP Request ( window = 0 )
TCP ACK ( window = 0 )
TCP ACK ( window = 0 )
Zero Window >= 3, Then drop or black list
X

## Slide 38: 智慧型威脅偵測與防護
Smarter Detection
Dynamic Mitigation
Extended Policy Actions
Protected Zones
Automated baselining
Progressive countermeasures
Including Verisign escalation
Superset of “ddos dst”

## Slide 39: 智慧型威脅偵測 : Automated Baselining
Sales Benefit
  Sell to organizations with limited security staff
Main Features
  Leverage multi-protocol counters providing deep visibility
  Apply this baseline intelligently to trigger security policies

## Slide 40: Baselining: Indicators and Threshold
Baselining /behavioral learning for detection
  Building traffic pattern profiles (peacetime learning) for
    Dst zone threshold
    Per source threshold
Threshold for automatic escalation
  Traffic pattern profile = zone-profile consists of multiple indicators with the threshold
Zone profile and individual threshold can be manually configured
TCP (incl. HTTP port) | 
Packet Rate SYN Rate FIN Rate RST Rate Small Window ACK Rate Empty ACK Rate | Small Payload Rate Bytes-to / Bytes-from SYN Rate / FIN Rate Session Miss Rate Packet Drop Rate Pkt Drop / Pkt Rcv’d Concurrent Sessions
UDP (incl. DNS port)
Packet Rate Packet Drop Rate Bytes-to / Bytes-from Pkt Drop / Pkt Rcv’d Concurrent Sessions
ICMP
Packet Rate Packet Drop Rate Bytes-to / Bytes-from Pkt Drop / Pkt Rcv’d
IP/Other
Packet Rate Packet Drop Rate Bytes-to / Bytes-from Pkt Drop / Pkt Rcv’d Fragment Rate
Notes: Packet, session, and ratio metrics enable comprehensive profiling and facilitate detection of anomalies

## Slide 41: 動態防禦政策: Progressive countermeasures
DDoS DST Zone
Thunder TPS
Level 0
Level 1
Level 2
Level 3
Level 4
DST
Mitigation Policy
Auto Learning (Baselining) or
Manual
Zone Threshold
Per SRC Threshold
可透過漸趨嚴格的對策來提高可疑流量的等級，以期盡可能減少誤判的發生

## Slide 42: Extended Policy Actions
Sales Benefit
  More flexibility for DevOps, or easy automation for limited staff
Main Features
  More elaborate action-lists
    Logging
    Capture packets
    Drop the packet
    Ignore – continue processing the packet
    Reset the connection
    Whitelist or blacklist the source
    Custom script execution using bash

## Slide 43: DDoS Dashboard - Incidents
List of incidents report for traffic visibility
Custom Incident
Auto created Incident

## Slide 44: DDoS Protection – Mitigation Console
Traffic Summary of the incident
Packet Debugger
Easy-access Mitigation Rule Setting
Traffic stats, indicators and Top-K

## Slide 45: Live Demo